## Slide 1: Qubit Placement to Minimize Communication Overhead in 2D Quantum Architectures
Alireza Shafaei, Mehdi Saeedi, Massoud Pedram
Department of Electrical Engineering
University of Southern California
Supported by the IARPA Quantum Computer Science Program
http://atrak.usc.edu/

## Slide 2: Outline
Introduction
  Quantum Computing Technologies
Geometric Constraints
  Nearest Neighbor Architectures
Proposed Solution
  MIP-based Qubit Placement
  Force-directed Qubit Placement
Results
Conclusion

## Slide 3: Quantum Computing
Motivation: Faster Algorithms
  Shor’s factoring algorithm (Superpolynomial)
  Grover’s search algorithm (Polynomial)
  Quantum walk on binary welded trees (Superpolynomial)
  Pell's equation (Superpolynomial)
  Formula evaluation (Polynomial)
Representation
Quantum
Algorithm
Quantum
Circuit
Physical
Realization
(PMD)
PMD: Physical Machine Description
http://math.nist.gov/quantum/zoo/

## Slide 4: Quantum Circuits
Qubits
  Data is carried by quantum bits or qubits
  Physical objects are ions, photons, etc.
Quantum Gates
  Single-qubit: H (Hadamard), X (NOT)
  Two-qubit: CNOT (Controlled NOT), SWAP
Quantum Circuit
H
X
q0
q1
q1
q0
q0
q1
q0
q1 q0
q0
q1
q2
X
q3

## Slide 5: Quantum PMDs
Move-based PMDs
  Explicit move instruction
    There are routing channels for qubit routing
  Examples: Ion-Trap, Photonics, Neutral Atoms
SWAP-based PMDs
  No move instruction
    There are no routing channels
  Qubit routing via SWAP gate insertion
  Examples: Quantum Dot, Superconducting
Focus of this presentation is on SWAP-based PMDs

## Slide 6: Geometric Constraints
Limited Interaction Distance
  Adjacent qubits can be involved in a two-qubit gate
  Nearest neighbor architectures
Route distant qubits to make them adjacent
  Move-based: MOVE instruction
  SWAP-based: insert SWAP gates
2
3
1
1
1
3
4
2
2
1
1
3
4

## Slide 7: SWAP-based PMDs
SWAP insertion
  Objective
    Ensure that all two-qubit gates perform local operations (on adjacent qubits)
  Side effects
    More gates, and hence more area
    Higher logic depth, and thus higher latency and higher error rate
  Minimize the number of SWAP gates by placing frequently interacting qubits as close as possible on the fabric
    This paper: MIP-based qubit placement
    Future work: Force-directed qubit placement (a more scalable solution)
MIP: Mixed Integer Programming

## Slide 8: Example on Quantum Dot
Simple qubit placement: place qubits considering only their immediate interactions and ignoring their future interactions
q0
q1
q2
X
q3
q4
CNOT
X
CNOT
CNOT
Two SWAP gates

## Slide 9: Example on Quantum Dot (cont’d)
Improved qubit placement: place qubits by considering their future interactions
q0
q1
q2
X
q3
q4
CNOT
X
CNOT
CNOT
No SWAP gate

## Slide 10: Qubit Placement
Assign each qubit to a location on the 2D grid such that frequently interacting qubits are placed close to one another
: assignment of to location
: assignment of to location
: number of 2-qubit gates working on and
: Manhattan distance between locations and
(1)
Min
subject to
,
,
.

## Slide 11: Kaufmann and Broeckx’s Linearization
Min
subject to
,
,
binary variables (), real variables (), and constraints
R. E. Burkard, E. ela, P. M. Pardalos, and L. S. Pitsoulis. The Quadratic Assignment Problem. Handbook of Combinatorial Optimization, Kluwer Academic Publishers, pp. 241-338, 1998.
(2)

## Slide 12: MIP Optimization Framework
GUROBI Optimizer 5.5 (http://www.gurobi.com)
  Commercial solver with parallel algorithms for large-scale linear, quadratic, and mixed-integer programs (free for academic use)
  Uses linear-programming relaxation techniques along with other heuristics in order to quickly solve large-scale MIP problems
Qubit placement (the MIP formulation) does not guarantee that all two-qubit gates become localized; Instead, it ensures the placement of qubits such that the frequently interact qubits are as close as possible to one another
  SWAP insertion

## Slide 13: SWAP Insertion
7
2
9
3
1
6
4
5
8
CNOT 1, 2
CNOT 5, 8
CNOT 3, 7
CNOT 2, 4
CNOT 6, 8
CNOT 1, 3
CNOT 2, 6
3
7
9
2
1
6
4
5
8
CNOT 1, 2
CNOT 5, 8
CNOT 3, 7
SWAP 2, 7
SWAP 2, 3
CNOT 2, 4
CNOT 6, 8
CNOT 1, 3
CNOT 2, 6
3
7
9
1
2
6
4
5
8
CNOT 1, 2
CNOT 5, 8
CNOT 3, 7
SWAP 2, 7
SWAP 2, 3
CNOT 2, 4
CNOT 6, 8
SWAP 1, 2
CNOT 1, 3
CNOT 2, 6

## Slide 14: Solution Improvement (1)
Two qubits may interact with one another at different times
  Not satisfactorily captured by a global qubit placer
  Solution: Partition the circuit into sub-circuits ()
(1) The placement tool finds initial qubit placements ().
(2) A SWAP insertion block generates final qubit placements () by inserting intra-set SWAP gates.
(3) A swapping network inserts inter-set SWAP gates to change the final placement of to the initial placement of as generated by the qubit placer

## Slide 15: Solution Improvement (2)
In the previous solution, is obtained without considering , for
  Large swapping networks
  Objective function of (1) only minimizes the intra-set communication distances
  Solution: Add a new term to the objective function in order to capture inter-set communication distances
: qubit in sub-circuit
: assignment of to location
: assignment of to location
: number of 2-qubit gates working on and

## Slide 16: Improved Qubit Placement
Min
subject to
,
,
.
(3)
Intra-set communication distance
Inter-set communication distance

## Slide 17: Force-directed Qubit Placement
Attractive forces
  A force proportional to between and .
  A (unit) force between between and .
Can be solved by quadratic programming

## Slide 18: Results (1)
 | # of qubits | # of gates | Grid Size | #SWAPs | #SWAPs | Imp. (%) | Ref.
3_17 | 3 | 13 | 2x2 | 6 | 4 | -50 | [1]
4_49 | 4 | 30 | 2x2 | 13 | 12 | -8 | [1]
4gt10 | 5 | 36 | 3x2 | 16 | 20 | 20 | [1]
4gt11 | 5 | 7 | 2x3 | 2 | 1 | -100 | [1]
4gt12 | 5 | 52 | 3x2 | 19 | 35 | 46 | [1]
4gt13 | 5 | 16 | 3x3 | 2 | 6 | 67 | [1]
4gt4 | 5 | 43 | 2x3 | 17 | 34 | 50 | [1]
4gt5 | 5 | 22 | 3x3 | 8 | 12 | 33 | [1]
4mod5 | 5 | 24 | 2x3 | 11 | 9 | -22 | [1]
4mod7 | 5 | 40 | 3x3 | 13 | 21 | 38 | [1]
aj-e11 | 4 | 59 | 2x3 | 24 | 36 | 33 | [1]
alu | 5 | 31 | 2x3 | 10 | 18 | 44 | [1]
decod24 | 4 | 9 | 2x2 | 3 | 3 | 0 | [1]
ham7 | 7 | 87 | 3x3 | 48 | 68 | 29 | [1]
hwb4 | 4 | 23 | 3x3 | 9 | 10 | 10 | [1]
hwb5 | 5 | 106 | 3x2 | 45 | 63 | 29 | [1]
hwb6 | 6 | 146 | 2x3 | 79 | 118 | 33 | [1]
hwb7 | 7 | 2659 | 3x3 | 1688 | 2228 | 24 | [1]
hwb8 | 8 | 16608 | 3x3 | 11027 | 14361 | 23 | [1]
hwb9 | 9 | 20405 | 4x3 | 15022 | 21166 | 29 | [1]
mod5adder | 6 | 81 | 3x2 | 41 | 51 | 20 | [1]
mod8-10 | 5 | 108 | 3x3 | 45 | 72 | 38 | [1]
rd32 | 4 | 8 | 2x3 | 2 | 2 | 0 | [1]
rd53 | 7 | 78 | 5x2 | 39 | 66 | 41 | [1]
rd73 | 10 | 76 | 4x4 | 37 | 56 | 34 | [1]
Our Method
Best 1D

## Slide 19: Results (2)
 | # of qubits | # of gates | Grid Size | #SWAPs | #SWAPs | Imp. (%) | Ref.
sym9 | 10 | 4452 | 4x4 | 2363 | 3415 | 31 | [1]
sys6 | 10 | 62 | 4x4 | 31 | 59 | 47 | [1]
urf1 | 9 | 57770 | 3x3 | 38555 | 44072 | 13 | [1]
urf2 | 8 | 25150 | 2x4 | 16822 | 17670 | 5 | [1]
urf5 | 9 | 51380 | 3x3 | 34406 | 39309 | 12 | [1]
QFT5 | 5 | 10 | 3x2 | 5 | 6 | 17 | [1]
QFT6 | 6 | 15 | 2x3 | 6 | 12 | 50 | [1]
QFT7 | 7 | 21 | 5x2 | 18 | 26 | 31 | [1]
QFT8 | 8 | 28 | 4x2 | 18 | 33 | 45 | [1]
QFT9 | 9 | 36 | 3x3 | 34 | 54 | 37 | [1]
QFT10 | 10 | 45 | 5x3 | 53 | 70 | 24 | [1]
cnt3-5 | 16 | 125 | 3x6 | 69 | 127 | 46 | [2]
cycle10_2 | 12 | 1212 | 3x4 | 839 | 2304 | 64 | [2]
ham15 | 15 | 458 | 5x3 | 328 | 715 | 54 | [2]
plus127mod8192 | 13 | 65455 | 5x4 | 53598 | 151794 | 65 | [2]
plus63mod4096 | 12 | 29019 | 5x3 | 22118 | 61556 | 64 | [2]
plus63mod8192 | 13 | 37101 | 5x3 | 29835 | 82492 | 64 | [2]
rd84 | 15 | 112 | 5x3 | 54 | 148 | 64 | [2]
urf3 | 10 | 132340 | 4x3 | 94017 | 154672 | 39 | [2]
urf6 | 15 | 53700 | 5x3 | 43909 | 88900 | 51 | [2]
Shor3 | 10 | 2076 | 4x3 | 1710 | 1816 | 6 | [3]
Shor4 | 12 | 5002 | 3x6 | 4264 | 4339 | 4 | [3]
Shor5 | 14 | 10265 | 5x4 | 8456 | 10760 | 21 | [3]
Shor6 | 16 | 18885 | 4x6 | 20386 | 20778 | 2 | [3]
 |  |  |  | On average |  | 27 | 
Our Method
Best 1D

## Slide 20: Results (3)
Improvement over best 1D solution

## Slide 21: Conclusion
Qubit placement methods for 2D quantum architectures
  Directly applicable to Quantum Dot PMD
27% improvement over best 1D results
Future work: force-directed qubit placement
  Better results by considering both intra- and inter-set SWAP gates in the optimization problem

## Slide 22: References
[1] A. Shafaei, M. Saeedi, and M. Pedram, “Optimization of quantum circuits for interaction distance in linear nearest neighbor architectures,” Design Automation Conference (DAC), 2013.
[2] M. Saeedi, R. Wille, R. Drechsler, “Synthesis of quantum circuits for linear nearest neighbor architectures,” Quantum Information Processing, 10(3):355–377, 2011.
[3] Y. Hirata, M. Nakanishi, S. Yamashita, Y. Nakashima, “An efficient conversion of quantum circuits to a linear nearest neighbor architecture,” Quantum Information & Computation, 11(1–2):0142–0166, 2011.

## Slide 23
Thank you!