## Slide 1
Energy-Efficient Cache Memories using a Dual-Vt 4T SRAM Cell with Read-Assist Techniques
Alireza Shafaei and Massoud Pedram
Department of Electrical Engineering
University of Southern California
Presented by Prof. Ali Afzali-Kusha
http://sportlab.usc.edu

## Slide 2: Outline
Introduction
Proposed dual-Vt 4T SRAM cell
Challenges
  Read operation using assist techniques
  Half-selected cells
    Selective row address decoder
Simulation results
Conclusion

## Slide 3: Introduction
Small area footprint of an SRAM cell results in:
  High memory density (# of bits per unit area)
  Shorter WLs and BLs  smaller wire resistances and capacitances  faster access delays and lower access energy consumptions
Minimum-size transistors are preferred in SRAM cell designs
  For FinFET technology: single-fin devices
Notes: The layout area of an SRAM cell is important because of two reasons:
Smaller cell layout results in higher memory density which means we can have larger number of bits in the chip
Smaller cell layout decreases the length of WL and BL, which in turn reduces their wire resistance and capacitance. As a result, we will have faster access latency and lower access energy.
Because of these reasons, minimum size transistors are preferred in SRAM designs. For FinFET technology, this is equivalent to use only single-fin devices in the SRAM design.

## Slide 4: Standard 6T SRAM Cell
Read stability (non-destructive read) requirement:
  During read, access transistor should be weaker than pull-down transistor
Write-ability (successful write) requirement:
  During write, access transistor should be stronger than pull-up transistor
M1 -- M4: two cross-coupled inverters to statically store data.
M5 & M6: access transistors to read from and write into the memory cell
Notes: The standard SRAM cell, as shown in this slide, is composed of six transistors:
* Four transistors (including two pull-up and two pull-down transistors) form two cross-coupled inverters which statically store data,
* Two access transistors used for reading from and writing into the memory cell.
Since read and write operations share access transistors, for proper read and write operations we should meet the following requirements
The read stability requirement to ensure a non-destructive read operation
The write-ability requirement to have a successful write operation

## Slide 5: Robust SRAM cells
SRAM cells which are robust against the increased effect of process variations in advanced technologies are needed
  8T, 9T, 10T, etc. SRAM cells
    Increase the cell area
  The all-single-fin 6T SRAM equipped with assist techniques, operating at low Vdd levels
    Adopted by Intel, TSMC, Samsung
  To further reduce the layout area and leakage power of the SRAM cell
    A dual-Vt 4T SRAM cell
Notes: Theses requirements may fail under process variations which are becoming very important in advanced technology node due to:
Extremely small geometries where even small deviations may significantly change device properties
Reduced Vdd levels which narrow the difference between Vdd and
Therefore, robust SRAM cells are needed, which can be achieved by:
Sizing up the transistors. For example, using 2 fins for pull-down transistors and I fin for access transistor, increases the read stability.
Using more robust cell structures such as 8T, 9T, 10T, etc.
These solutions increase the layout area of the SRAM cell. Hence, major semiconductor industries such as Intel, Samsung, and TSMC, are adopting 6T SRAM with all single-fin devices, operating at low-Vdd levels to reduce the power consumption, and stability requirements are improved by assist techniques.
In this presentation, to further reduce the area and leakage power of the all-single-fin 6T SRAM, we propose a 4T SRAM cell based on dual-Vt FinFET devices.

## Slide 6: Proposed Dual-Vt 4T SRAM Cell
Based on 4T driverless structure
Dual-Vt design:
  Low-Vt (LVT) devices for access transistors
  Ultra-high-Vt (UVT) devices for pull-up transistors
  Resolves the low hold stability and high leakage power of previously-published 4T SRAM cells
Notes: The proposed 4T SRAM cell is shown in this slide, which is based on 4T driverless design. What makes our cell different from prior work, is its dual-Vt design which is important for
High stability of hold operation
Improving write operation, and
Reducing the leakage power
Therefore, unlike other 4T designs which mainly suffer from high leakage power, the leakage power of our proposed cell is at least 2× smaller than that of its 6T counterpart.

## Slide 7: Cell Layout
Cell | Area | Aspect Ratio
6T |  | 0.4
4T [1] |  | 0.3
4T (ours) |  | 0.83
Cell | Area | Aspect Ratio
6T |  | 0.4
4T [1] |  | 0.3
4T (ours) |  | 0.83
6T
4T [1]
4T (ours)
PM: metal pitch
[1] M.-L. Fan et al., “Comparison of 4T and 6T FinFET SRAM Cells for Subthreshold Operation Considering Variability—A Model-Based Approach,” IEEE Transactions on Electron Devices, March 2011.
Closer to a square
4T is 25% smaller than 6T (using only single-fin devices)
Notes: Layouts of 6T (all-single-fin) and 4T are shown in this slide. For 4T, we show two layouts: one proposed in [1], and our proposed layout.
The table compares area and aspect ratio of cells. Pm in this table refers to the metal pitch.
Both 4T layouts are 25% smaller than the 6T.
However, the aspect ratio of our cell is closer to one. Hence, our proposed layout is closer to a square.

## Slide 8: Hold Operation
4T is a semi-static memory cell
  UVT devices are extremely low leakage.
  Bitlines are 0 during hold operation.
  Higher leakage current of (LVT) access transistors than that of (UVT) pull-up transistors, keeps the dynamic node discharged during hold.
For a 4T SRAM storing bit 0:
Q floats (a dynamic storage node)
QB is statically connected to Vdd
Very low leakage
Due to higher leakage current and V(BL) = 0, Q (dynamic node) is kept discharged
Notes: 4T is a semi-static memory. Because during the hold operation, and depending on the cell content, one storage node (QB in this slide) is statically connected to Vdd through one of the pull-up transistors, whereas the other node (Q) floats and acts as a dynamic storage node.
The dynamic node should be kept discharged during the idle mode in order to make sure that data is properly retained. For this purpose, bitlines are pulled to Gnd.
Also, by assigning low-Vt (LVT) devices to access transistors, and high-Vt (HVT) devices to pull-up transistors, access transistors have a higher leakage current than pull-up transistors. Therefore, access transistors are able to keep the dynamic node discharged during idle mode.
To improve the hold stability, leakage current of the pull-up transistors should be very small. Thus, we use ultra-high-Vt (UVT) devices for pull-up transistors.
UVT devices in FinFET technology can be fabricated by engineering the work function of the gate material. This allows us to aggressively increase the Vt of the FinFET device. An important feature of this approach is that it does not impact the cell layout area.

## Slide 9: Write Operation
The proposed 4T SRAM has a fast and reliable write operation:
  LVT devices have higher ON current than UVT devices
  Lack of pull-down transistors also helps in improving the write operation
    No fight when writing into the dynamic node
Notes: Since fast LVT devices are used for access transistors, and slow UVT devices are used for pull-up transistors, access transistors are stronger than pull-ups, which facilitates write operation.
Also, the lack of pull-down transistors helps in improving the write operation. The reason is because the access transistor, when turned on, can easily write into the dynamic storage node.
All these features point to a reliable and fast write operation.

## Slide 10: Challenges
Destructive read operation
  Should weaken the access transistor and/or strengthen the pull-up transistor during the read operation
    Read-assist techniques
Low stability of half-selected cells
  Selective row address decoder
    Only activates the wordline of accessed cells
Notes: There are two important challenges:
Our dual-Vt design results in a destructive read operation (because access is stronger than pull-up, and hence, during read, access will flip the cell content). To resolve this issue, we use read-assist techniques to weaken access transistor and strengthen pull-up transistor.
Half-selected cells (HSCs) in semi-static memories generally suffer from an undesired write operation (details will be explained later). Our solution is to only activate the WL of accessed cells. For this purpose, we design a selective row address decoder.

## Slide 11: Read Operation using Assist Techniques
To achieve a non-destructive read operation, we simultaneously apply the following read-assist techniques:
  Wordline underdrive (WLUD)
    Decreases the voltage level of wordline
    Hence, weakens the access transistor
  Vdd boost (VDDB)
    Increases the cell supply voltage
    Thus, strengthens the pull-up transistor
Notes: We have to apply both techniques, discussed here, otherwise we cannot achieve a high read SNM.
The figure illustrates adopted read-assist techniques.
Also, during read, bitlines are pre-discharged to 0.

## Slide 12: Half-selected Cells (HSCs)
An HSC refers to an idle cell in which the value of a control signal has been changed because of a read or write operation on a different cell.
Due to very fast write operation in our 4T, the value of the dynamic node cannot be destroyed.
An undesired write operation happens which puts row HSCs into a metastable state.
Notes: Definition of an half-selected cell (HSC).
In the figure, we assume that we are going to access the top-left cell for a write-1 operation.
The other two cells are now HSCs:
* Bottom-left cell is a column HSC (since it is on the same column as the accessed cell).
* Top-right cell is a row HSC (because it is on the same row as the accessed cell).
For the column HSC shown here, voltage of BL becomes Vdd. Therefore, This may cause a problem for the dynamic node. However, since access transistors of column HSCs are turned off, and because write operation is very fast in our proposed cell, the value of the dynamic node cannot be destroyed (Moreover, based on our simulations, the voltage level drop of the dynamic node under column half-select disturbance and for a time period 1000 times longer than the write access latency is less than 1%).
The main problem is the row HSC. For row HSCs, the voltage of WL becomes Vdd, which means their wordline is now activated, and this causes an desired write-0 in the static node. This puts the SRAM into metastability.

## Slide 13: Selective Row Address Decoder
To avoid the undesired write in row HSCs:
  Activate only the wordline of accessed cells
Notes: To avoid this undesired write in row HSCs, we modify the row address decoder such that only the WL of accessed cells is activated.
The circuit of the proposed selective row address decoder is shown in this slide, which also receives inputs from the column decoder.
A word refers to a group of cells which will be read or written in the same cycle.

## Slide 14: Simulation Setup: FinFET Devices
Adopted FinFET library:
  Physical gate length = 7nm
  Nominal Vdd = 0.45V
  Includes LVT, high-Vt (HVT), and UVT devices
  http://sportlab.usc.edu/downloads/download/
Notes: Specifications of the adopted FinFET devices are presented in this slide.

## Slide 15: Simulation Setup: SRAM Cells
SRAM cells (using only single-fin devices):
  4T SRAM cell
    Access transistors = LVT, pull-up transistors = UVT
  6T SRAM cell
    LVT devices for all transistors
SRAM cell characteristics:
  Hold and read SNMs:
    Measured based on butterfly curves
  Write margin:
    The difference between the Vdd and the minimum wordline voltage that is needed to flip the cell content
  Yield analysis:
    Monte Carlo simulations with 2000 samples
    is adopted for a high-yield SRAM cell
Notes: Our 4T SRAM cell is compared with the all-single-fin 6T SRAM.
For each SRAM, the following characteristics are measured using HSpice simulations:
Hold and read SNMs which are measured based on butterfly curves.
Write margin. The definition is given.
Also, to analyze the yield of SRAM cells, we perform Monte Carlo simulations on 2,000 samples. We assume a mu over sigma greater than or equal to 6 is needed to have a high yield SRAM cell.

## Slide 16: Simulation Setup: Process Variations
Process variations on the adopted FinFET devices are modeled as follows:
A voltage source to inject variations on the threshold voltage
A current source to introduce variations on the saturation current
[2] P. Royer and M. Lopez-Vallejo, “Using pMOS Pass-Gates to Boost SRAM Performance by Exploiting Strain Effects in Sub-20-nm FinFET Technologies,” IEEE Transactions on Nanotechnology, Nov 2014.
Notes: The adopted 7nm FinFET devices are lookup table-based Verilog-A models, which are generated for nominal conditions.
Process variations are then modeled by variations on the threshold voltage and drain-to-source current, as follows. Each transistor of the SRAM cell is modeled as the circuit shown in this slide. In other words, for each transistor:
A voltage source is inserted on the gate terminal in order to inject variations on the threshold voltage, and
A current source is added between drain and source terminals in order to introduce variations on the saturation current.

## Slide 17: Simulation Setup: Cache Memories
FinCACTI tool is used to derive the characteristics of FinFET-based cache memories
  L1: 32KB, 2-way set-associative
  L2: 256KB, 8-way set-associative
: access ratio
: dynamic power
: leakage power
: access frequency
: total power
: energy per cycle
Notes: FinFET-based cache memories are characterized using the FinCACTI tool.
Access ratio is measured using SNIPER.
Dynamic power, leakage power, and access frequency are measured using FinCACTI.
Finally, total power consumption and per cycle energy consumption are calculated as shown here.

## Slide 18: Cell-Level Results: Noise Margins
Notes: Noise margins of 4T and 6T cells are reported in this table:
* For hold: both SRAMs achieve high hold SNM.
* For write: 6T requires an assist technique (wordline overdrive is used in this paper) to achieve high write margin. 4T does not need any write assist techniques.
* For read: Both 4T and 6T need assist techniques. However, 4T without assist cannot read. Hence, more aggressive read-assist techniques (higher voltages) are needed for the 4T. This increases the dynamic power of the 4T compared with the 6T.

## Slide 19: Cell-Level Results: Leakage Power
Notes: In this figure, leakage power of 6T is shown for different Vdd levels. The leakage power of 4T for the nominal Vdd (045V) is also shown for comparison purposes.
As we can see, at 0.45V and 0.3V, leakage of 6T is 3.5x and 2.2x, respectively, larger than that of 4T.
Even at 0.15V, the leakage power of 6T is 25% higher than that of 4T at 0.45V. This shows the effectiveness of the proposed 4T SRAM cell design in reducing the leakage power which is especially crucial for high-capacity cache memories.

## Slide 20: Cache-Level Results
4T has higher dynamic power because of more aggressive read-assist techniques.
Notes: Cache-level results are reported here.
4T has lower leakage power and faster access frequency. The lower leakage power is more important for L2 cache, which has more SRAM cells and its activity factor is small.
However, 4T has higher dynamic power. As a result, the total power of 4T is larger than that of 6T for L1.

## Slide 21: Conclusion
4T SRAM cell compared with 6T counterpart
  25% smaller layout area
  Our dual-Vt design also achieves
    High hold stability due to negligible leakage current of the UVT pull-up transistors
    3.5x smaller leakage power at the nominal Vdd
    But has higher dynamic power because of aggressive read-assist techniques
    Overall:
      For L1 cache: 18% lower energy consumption with 35% higher access frequency
      For L2 cache: 2x lower energy consumption with 19% higher access frequency

## Slide 22
Thank you!